## Slide 1: Recreational Fire Pit Emissions Testing
Shawn Urbanski, Emily Lincoln, Steve Baker, Bryce Nordgren
USDA Forest Service, Rocky Mountain Research Station
Anne Jackson, Minnesota Pollution Control Agency
US EPA 2023 International Emissions Inventory Conference
Seattle, WA
September 28, 2023

## Slide 2: Motivation and Study Questions
Study Questions
Do “low-smoke” fire pits have lower PM2.5 emission factors (EFPM) than traditional fire pits?
Provide data for estimating PM2.5 emissions from “low-smoke” outdoor recreational fire pit use in Minnesota
What is effect of firewood moisture content (MC) on PM emissions?
Motivation
Initiated and Funded by the Minnesota Pollution Control Agency (MPCA)
Sales of woodburning outdoor recreational wood burning equipment (ORE) – fire pits – have increased significantly since COVID-19 pandemic
Anecdotal evidence of increased use of backyard fire pits in urban/suburban areas
Increased consumer demand for “smokeless” fire pits

## Slide 3: Recreational Firepit Emissions Testing
Fuel
Consumption
Emission Rate
Emission Factor
=

EFPM
(g-PM2.5/kg-fuel consumed)
FC
(kg-fuel consumed/hour)
EPM
(g-PM2.5/hour)
=

Measure EFPM, FC and other factors to estimate EPM for firepit use
FC, a function of user behavior, will drive emissions
Need to: Standardize FC across tests
Extrapolate test results to real world use
Recreational Fire Pit Emissions Testing

## Slide 4: Fire Pits Tested
Solo Yukon
Breeo
Pilot Rock
“Low-smoke” Fire Pits
3/16” thick steel
8” high heat shield with cooling air gap.
32” diameter
Accessible Campground Fire Ring
304 stainless steel
38 pounds
27” diameter
17” height
304 stainless steel
62 pounds
24” diameter
16” height
Recreational Fire Pit Emissions Testing

## Slide 5: Fuels
Recreational Fire Pit Emissions Testing
Split firewood, red oak, maple, and birch, from Minnesota
Round 1
May 2019
Moderate to low moisture content (MC)
Round 2
June 2021
MC 14-35%
Round 3
December 2019
MC 6-9%
MC 20-27%
Same fuel as round 1, cured for 9 months
New pallet of wood, uncured

## Slide 6: USDA Forest Service Combustion Facility
Mixing ratio & T uniform across the width of the stack
Diffuser ring mixes the air and entrained emissions
Outdoor air into chamber at floor along the walls and exhausted through stack
Firepit centered under intake funnel of exhaust stack
12.5 m
17 m
sa
firepit
exhaust fan
Sampling
platform
1.6 m
diffuser orifice
Radiometer
Gas & particle sampling
Gas & aerosol instruments sample emissions + ambient air
Instruments on chamber floor measure radiant heat flux, T, RH, CO2
Recreational Fire Pit Emissions Testing

## Slide 7: Setup
Background
CO2 measurement
Fire Pit
Radiant heat flux
measurement
Radiant heat flux
measurement
43 inches
27 inches
27 inches
Sampling Platform
Emissions instrumentation on the sampling platform
Measure PM, CO2, CO, CH4
Combustion Chamber Floor
The firepit under the center of the exhaust stack
Radiant heat sensors on two sides
Gas analyzer monitored the background CO2 concentration.
Recreational Fire Pit Emissions Testing
Continuous measurement
CO2, CO, CH4 via
Cavity Ring-down Spectroscopy

## Slide 8: Quantifying EF
Recreational Firepit Emissions Testing
Carbon Mass Balance Method
All volatilized carbon species measured
Emissions are well mixed
volatilized fuel C% = unburnt fuel C%
Excess mixing ratio = Emissions
Fc = Fuel carbon fraction (C%)
CT = Sum of volatilized carbon
> 90% of volatilized C in CO2, CO, and CH4

## Slide 9: Burn cycle
Recreational Fire Pit Emissions Testing
Burnup Stage
Fuel additions 5 min.
Duration 25 min.
Fuel added 15 kg
Fuel additions 10 min.
Duration 55 min.
Fuel added 11 kg
Begins 10 min. after last steady stage fueling
Duration 25 min.
Steady Burn Stage
Burndown Stage
Typical recreational use
Achieve steady fire
Smoldering
Fuel additions weighed. Periodically reserve fuel for moisture content. Extinguish to preserve charcoal & unburnt fuel

## Slide 10: Typical burn profile
Recreational Firepit Emissions Testing
Round 1, May 10, 2019
Solo Firepit (MC = 14%)

## Slide 11: PM2.5 Emission Factors
Recreational Fire Pit Emissions Testing
Burn-up
Steady-burn
Burn-down
 | Burn-up | Steady- burn | Burn-down
EFPM (g kg-1) |  |  | 
Solo | 2.8 | 2.0 | 1.5
Breeo | 3.6 | 1.8 | 1.6
Pilot | 3.6 | 2.5 | 1.7
All | 3.4 | 2.1 | 1.6
No. tests = 31, Moisture Content: 6 – 35%

## Slide 12: EFPM2.5: “low-smoke”/barrel design fire pits versus AP-42 and pile burns of logging slash
Recreational Fire Pit Emissions Testing
AP-42 from Houck et al. (2001)
Pile burns from Wright et al. (2010)
“low-smoke” / barrel design fire pits  2.2 g kg-1
AP-42 (outdoor woodburning device)  11.8 g kg-1
Pile burn of logging slash = 6.8 g kg-1
Steady-burn
stage

## Slide 13: Does firewood moisture content influence EFPM?
Recreational Fire Pit Emissions Testing
Steady-burn Stage
y = 1.5 + 0.04x
R2 = 0.12, p-value = 0.056
No strong influence for steady-burn stage
Not enough tests to sort fire pit/MC effects
MC does impact burn-up stage:
EFPM increases with MC
Burn-up

## Slide 14: Weighting combustion phases for single EF based on firewood input
Recreational Fire Pit Emissions Testing
Create model of typical burn:
Test data – EF, firewood addition rate, combustion completeness
Assumptions for typical burn –
Similar fueling approach and appliance
Split hardwood at MC = 15%
Burn stage durations (minutes) –
Burn-up = 20, Steady-burn = 120, Burn-down = 60
consumed
Firewood addition & combustion
Weighted EF = 2.0 g kg-1 (4.0 lb ton-1)

## Slide 15: Emission Inventory Impact
Recreational Fire Pit Emissions Testing
Replacing 1 fire pit provides  7 lb y-1 reduction in PM
1 pp increase ‘low-smoke’ ORE = 1.24% reduction in emissions
Minnesota residential wood combustion survey MSP Metro region estimates for 2018:
# Outdoor Recreational Equipment (ORE) = 358,371
Annual wood use = 0.25 cord/piece = 0.363 ton/piece
Annual PM2.5 = 1533 ton (EFPM = 23.6 lb/ton)
Our ‘typical burn’ implies  9 burns / year/ ORE

## Slide 16: Conclusions
EFPM for “low-smoke”/barrel design fire pits 80% lower than AP-42
PM emissions normalized to radiant heat flux increase with MC
Higher MC  lower radiant heat yield  greater firewood use  more emissions
Improved MC handling and increased test number would have reduced uncertainty in emissions prediction

## Slide 17: Additional Questions
How does real world fire pit activity compare with standardized fueling used in testing?
How do fire pits used in testing compare versus other designs?
Small EFPM difference between “low smoke” & Pilot suggests physical dimensions are important factor

## Slide 18: THANK YOU QUESTIONS?
Recreational Fire Pit Emissions Testing